JOINT ELECTRICITY REGULATORY COMMISSION

FOR MANIPUR AND MIZORAM

AIZAWL : MIZORAM

TBL Bhawan, 2nd –5th Floor, E-18, Peter Street, Khatla, Aizawl, Mizoram - 796001

Fax: 0389-2301299/2300240, Tel. No. : 0389-2310623/2320555

Website: www.jerc.mizoram.gov.in, Email: jerc.mm@gmail.com

D R A F T     N O T I F I C A T I O N

Dated Aizawl, the 22nd August, 2022

No.H.13011/36/16-JERC: In exercise of powers conferred under Section 50 read with Clause (x) of Sub-section (2) of Section 181 of the electricity Act, 2003 (36 of 2003), and all other powers enabling it in this behalf, the Joint Electricity Regulatory Commission for Manipur & Mizoram hereby makes the following regulations to amend the Joint Electricity Regulatory Commission for Manipur & Mizoram (Metering for Grid Connected Renewable Energy) Regulations, 2016 (herein referred to as “Principal Regulations”), namely;

- Short title and commencement:-

- This Regulation may be called the draft Joint Electricity Regulatory Commission for Manipur & Mizoram (Metering for Grid Connected Renewable Energy)(Second Amendments) Regulation, 2022.

- This Regulation shall extend to the whole States of Manipur & Mizoram and shall apply in relation to all matters falling within the jurisdiction of the Commission.

- This Regulation shall come into force from the date of their notification in the Official Gazette of the concerned States.

- Amendments in Regulation 2.1 of the Principal Regulations:-

- Sub-clause (21) shall be inserted just after the existing entry of sub-clause (20) as below:

‘(21)“prosumer’ means a person who consumes electricity from the grids and can also inject electricity into the grid for distribution licensee, using same point of supply.’

- The following sub-clause numbers of the Principal Regulations shall be read and corrected respectively as below:

‘(21) as (22), (22) as (23), (23) as (24), (24) as (25), (25) as (26), (26) as (27), (27) as (28), (28) as (29), (29) as (30) and (30) as (31).’

- Amendments in Regulation 4 of the Principal Regulations:-

Clauses 4.2 and 4.3 shall be inserted just after Clause 4.1 as below:

‘4.2	The  distribution  licensee  shall  facilitate  the  process  for  setting  up  of RE

generation systems at prosumers’ premises. In this regard, the licensee shall –

(1) create  an  online  portal  for  receiving  applications  from  prosumers  for

installation,  interconnection and metering of distributed renewable energy

systems  or  devices  at  their premises, and update the same on a regular

basis;

(2) prominently  display  on  its  website  and  in  all  its offices, the following;

namely:-

(i) detailed  standardized  procedure for installation and commissioning

of roof top solar system;

(ii) a  designated  official  to  be  contacted  in  order  to  facilitate  the

consumers in installation of roof   top  solar  system  from  submission  of  application  form  upto commissioning.

(iii) address   and   telephone   numbers   of   offices   where  filled-up

application forms can be submitted;

(iv) complete  list  of  documents  required  to  be furnished along with

such applications;

(v) applicable charges to be deposited by the applicant;

(vi) empanelled  list  of  service  providers for the benefit of consumers

who  want  to  install  roof  top  solar  PV  system  through service

providers; and

(vii) financial  incentives  to the prosumers, as applicable under various

schemes and programmes of the Central and State Governments;

4.3	The distribution licensees shall ensure that –

(i) application  forms  shall  be  accepted  online or through hard copy;

(ii) in case the application form submitted in hard copy form, the same

shall  be  scanned  and  uploaded  on  the  website  as soon as it is

received  and  acknowledgement  with  the  registration number for

that application shall be generated and intimated to the applicant;

(iii) in  case  the application form received online through web portal of

the    distribution    licensee,    the    acknowledgement   with   the

registration    number    shall   be   generated   on   submission   of

application;

(iv) application   shall   be   deemed  to  be  received  on  the  date  of

generation of acknowledgement with registration number; and

(v) the    application   tracking   mechanism   based   on   the   unique

registration  number  shall  be  provided by the distribution licensee

through  web-based  application  or any other mode to monitor the

status  of  processing  of  the application like receipt of application,

site inspection, meter installation and commissioning, etc.’

- Amendments in Regulation 5 of the Principal Regulations:-

Clause 5.1 of the principal Regulations shall be substituted by the following:-

‘5.1	The  distribution  licensee  shall provide net or gross metering arrangement to

any  eligible  consumer  or  third  party owner as long as the total capacity (in

MW)  does  not  exceed the target capacity for meeting the annual Renewable

Purchase  Obligation  (RPO)  requirement determined by the Commission from

time to time.

Provided that the cumulative capacity of distribution renewable energy systems allowed to be interconnected with the distribution network (feeder / distribution transformer) shall not exceed 100% of the feeder and/or distribution transformer capacity, as applicable.

Provided further that the feeder/transformer mentioned above, considered for the purpose of the hosting capacity, shall mean the feeder / transformer owned by the distribution licensee.

- Amendments in Regulation 6 of the Principal Regulations:-

1) Clause 6.2 of the Principal Regulations shall be substituted by the following:

‘6.2	The maximum capacity of roof top solar PV system under net metering system

shall not exceed 10 (ten) kW and there is no such capacity restriction under gross metering system:

Provided that the installed capacity in respect of roof top solar energy system shall not be less than 1 kWp and shall not exceed 1 MWp (AC side) for a single eligible consumer;

Provided further that the roof top solar projects of rating higher than 500 kWp can be considered by the distribution licensee only if the distribution system stays stable subject to approval by the appropriate authority after undertaking inspection and safety checks;

Provided further that a variation in the rated capacity of the system within a range of five percent shall be allowed.

2) Clause 6.3 shall be added after Clause 6.2 of the Principal Regulation as below:

‘6.3	The  prosumer  is  allowed  to  set  up  roof  top  solar PV system with battery

storage.’

- Amendments in Regulation 7 of the Principal Regulations:-

1) 	Clause 7.6 of the Principal Regulations shall be substituted by the following:

‘7.6 During   the   inspection,   the   licensee  shall  assess  the  feasibility  for  grid

connection of the renewable energy system and shall verify all particulars mentioned in the application form and the documents as required and intimate the eligible consumer accordingly;

(1) The   details  of  additional  documents  to  be  submitted  by  the  eligible

consumer.

(2) Particulars of any deficiencies, if noticed, along with instructions to remove

such defects.

Provided that if there is any requirement of upgradation of distribution infrastructure such as augmentation of service line, distribution transformer capacity, etc., for installation of the required capacity of solar PV system, the same shall be carried out by the distribution licensee or consumer, as the case may be.’

2) 	Clauses 7.10, 7.11, 7.12, 7.13 and 7.14 shall be added after Clause 7.9 as below:

‘7.10	Consumer  shall  have  the  option  of  purchasing  the requisite meter himself

which shall be tested and installed by the distribution licensee.

7.11	The  timelines  as  specified  by  the  Commission  shall  be  adhered to by the

distribution licensee. In case of delay, the licensee shall take approval from the Commission in specific cases along with justification for the same.

7.12	In  case  of  any delay on the part of the distribution licensee without any just

cause, the licensee shall be liable to pay compensation to the consumer at a rate which shall not be less than five hundred rupees per day for each day of default.

7.13	The   energy   generated   by   prosumer   shall  be  adjusted  against  energy

consumed or the bill amount, depending on whether net metering or gross metering as applicable.

7.14	The   distribution   licensee   shall   pass   on  the  financial  incentives  to  the

Prosumers as applicable and as may be provided under various schemes and programmes of the Central and State Governments.’

- Amendments in Regulation 9 of the Principal Regulations:-

Clause 9.10 shall be substituted by the following:

‘9.10	Subject to sub-regulation 9.5 above, the distribution licensee may call upon the renewable energy generator to rectify the defect within a reasonable time.’

By Order of the Commission

Sd/-RICHARD ZOTHANKIMA

Secretary

Statement of Reason

Government of India notified the Electricity (Rights of Consumers) Rules, 2020 in the Gazette of India on 31st December, 2020. On issue of the above Rules, it is required to amend the relevant regulations to comply with the Rules. Therefore, the JERC for Manipur and Mizoram (Metering for Grid Connected Renewable Energy) Regulations, 2016 is hereby amended for compliance by all the stakeholders in Manipur and Mizoram.

Secretary