JOINT ELECTRICITY REGULATORY COMMISSION

FOR MANIPUR AND MIZORAM

AIZAWL : : : MIZORAM

TBL Bhawan, 2nd –5th Floor, E-18, Peter Street, Khatla, Aizawl, Mizoram - 796001

Fax: 0389-2301299/2300240, Tel. No. : 0389-2310623/2320555

Website: www.jerc.mizoram.gov.in, Email: jerc.mm@gmail.com

S T A F F   P A P E R

In the matter of:

Adoption of Central Electricity Regulatory Commission (Terms and Conditions for Tariff Determination from Renewable Energy Sources) Regulations, 2012 (CERC RE Regulations, 2012) and the amendments thereof and determination/fixation of generic levellised generation tariff RE technologies and for power projects using Municipal Solid Waste/Refuse Derived Fuel based on Ranking Cycle Technology.

- The Commission has notified the JERC for M&M (Terms and Conditions for Tariff Determination from Renewable Energy Sources) Regulations, 2010 on 31.05.2010 and the JERC for M&M (Terms and Conditions for Tariff Determination from Renewable Energy Sources) (First Amendment) Regulations, 2014 on 05.08.2014. These Regulations provide for terms and conditions and the procedure including various technical norms prescribed by the Regulations of Central Electricity Regulatory Commission (CERC) vide its notification No.L-1/94/CERC/2016, dated 6.02.2012 called CERC (Terms and Conditions for Tariff Determination from Renewable Energy Sources) Regulations, 2012 and vide its notification No.L-1/94/CERC/2011, dated 18.03.2014 called CERC (Terms and Conditions for Tariff Determination from Renewable Energy Sources) (First Amendment) Regulations, 2014. The Commission had determined generic levellised generation tariff for the FY 2014-15 on the basis of various norms specified in the above regulations vide its Order dated 05.01.2015 which is available in the JERC for Manipur and Mizoram website www.jerc.mizoram.gov.in.

- CERC vide Notification No.L-1/94/CERC/2011, dated 05.01.2015 amended the CERC RE Regulations, 2012 called CERC (Terms and Conditions for Tariff Determination from Renewable Energy Sources) (Second Amendment) Regulations, 2014 (Second Amendment, 2014) wherein Regulation 4(c) and Regulation 41 pertaining to the use of 15% fossil fuels by Biomass based Power Projects were amended. Further, CERC vide Notification No.L-1/94/CERC/2011, dated 10.07.2015 amended the CERC (Terms and Conditions for Tariff Determination from Renewable Energy Sources) (Third Amendment) Regulations, 2015 (Third Amendment, 2015) vide which ‘Regulation 38: Station Heat Rate’ (SHR) and ‘Regulation 43: Calorific Value’ (CV) for Biomass based Power Projects were amended. The revised norms in respect of SHR were specified as 4126 kCal/kWh for projects using travelling grate boilers & 4063 kCal/kWh for projects using AFBC boilers. The revised norms in respect of CV were specified as 3174 kCal/kg for Biomass based Power Projects using fossil fuel upto 15% of calorific contribution.

- CERC vide Notification No.L-1/94/CERC/2011, dated 07.10.2015 amended the CERC RE Regulations, 2012 called CERC (Terms and Conditions for Tariff Determination from Renewable Energy Sources) (Fourth Amendment) Regulations, 2015 (Fourth Amendment, 2015) vide which norms/parameters for Municipal Solid Waste (MSW) and Refuse Derived Fuel (RDF) based Power Projects have been specified and determined tariff for such projects. CERC vide Notification No.L-1/94/CERC/2011, dated 30.03.2016 amended the CERC RE Regulations, 2012 called CERC (Terms and Conditions for Tariff Determination from Renewable Energy Sources) (Fifth Amendment) Regulations, 2016 (Fifth Amendment, 2016) vide which the Normative O&M expenses for Solar PV Power Projects for FY 2016-17 was fixed at Rs. 7 lakhs/MW. The consolidated CERC RE Regulation amendments upto January incorporated and the Fifth Amendment, 2016 are available on CERC website www.cercind.gov.in

- .CERC has, in due discharge of the mandate under Regulation 8 of the CERC RE Regulations, 2012 determined the levellised generic tariff of RE Projects for the fifth year (FY 2016-17) of the control period in its Order dated 29.04.2016 in petition No.SM/03/2016 (Suo-Motu). This Order is available on the CERC website www.cercind.gov.in. As per this order, the generic tariff for the various RE Projects/Technologies to be commissioned during the year 2016-17 are as under:

Generic Tariff for RE technologies for FY 2016-17

| Levellised Fixed Cost (₹/kWh) | Variable Cost (FY 2016- 17) (₹/kWh) | Applicable Tariff Rate (₹/kWh) | Benefit of Accelerated Depreciation, if availed (₹/kWh) | Net Applicable Tariff Rate upon adjusting for Accelerated Depreciation benefit (3-4) (₹/kWh) |
| --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 |
| Biomass Power Projects [other than Rice Straw and Juliflora (plantation) based project] with Water Cooled Condenser and using travelling grate boiler |
| 3.10 | 4.39 | 7.49 | 0.18 | 7.31 |
| Biomass Power Projects [other than Rice Straw and Juliflora (plantation) based project] with Air Cooled Condenser and travelling grate boiler |
| 3.28 | 4.49 | 7.77 | 0.20 | 7.57 |
| Biomass Power Projects [Rice Straw and Juliflora (plantation) based project] with Water Cooled Condenser and travelling grate boiler |
| 3.24 | 4.39 | 7.62 | 0.20 | 7.43 |
| Biomass Power Projects [Rice Straw and Juliflora (plantation) based project] with Air Cooled Condenser and travelling grate boiler |
| 3.42 | 4.49 | 7.91 | 0.22 | 7.70 |
| Biomass Power Projects [other than Rice Straw and Juliflora (plantation) based project] with Water Cooled Condenser and AFBC boiler |
| 3.09 | 4.32 | 7.41 | 0.18 | 7.23 |
| Biomass Power Projects [other than Rice Straw and Juliflora (plantation) based project] with Air Cooled Condenser and AFBC boiler |
| 3.27 | 4.42 | 7.69 | 0.20 | 7.50 |
| Biomass Power Projects [Rice Straw and Juliflora (plantation) based project] with Water Cooled Condenser and AFBC boiler |
| 3.23 | 4.32 | 7.55 | 0.20 | 7.35 |
| Biomass Power Projects [Rice Straw and Juliflora (plantation) based project] with Air Cooled Condenser and AFBC boiler |
| 3.42 | 4.42 | 7.84 | 0.22 | 7.62 |
| Bagasse Based Co-generation Project |
| 2.79 | 3.36 | 6.14 | 0.21 | 5.94 |
| Non-Fossil Fuel based Co-Generation Projects |
| 2.79 | 3.36 | 6.15 | 0.21 | 5.94 |
| Biomass Gasifier Power Projects |
| 2.64 | 4.17 | 6.81 | 0.13 | 6.68 |
| Biogas based Power Projects |
| 4.09 | 3.59 | 7.68 | 0.26 | 7.42 |

| Particulars | Applicable Tariff Rate (₹/kWh) | Benefit of Accelerated Depreciation, if availed (₹/kWh) | Net Applicable Tariff Rate upon adjusting for Accelerated Depreciation benefit (2-3) (₹/kWh) |
| --- | --- | --- | --- |
| 1 | 2 | 3 | 4 |
| Small Hydro Power Projects |
| Below 5 MW | 4.70 | - | - |
| 5 to 25 MW | 3.99 | - | - |
| Wind Energy Power Projects |
| Wind Zone-1 | 6.60 | 0.71 | 5.89 |
| Solar Power Projects |
| Solar PV | 5.68 | 0.60 | 5.08 |
| Solar Thermal | 12.07 | 1.25 | 10.82 |

The generic tariff for MSW based power projects and RDF based MSW power projects for FY 2016-17 are as under:

| Levellised Fixed Cost (₹/kWh) | Variable Cost (FY 2015- 16) (₹/kWh) | Applicable Tariff Rate (₹/kWh) | Benefit of Accelerated Depreciation, if availed (₹/kWh) | Net Applicable Tariff Rate upon adjusting for Accelerated Depreciation benefit (3-4) (₹/kWh) |
| --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 |
| MSW based Power Projects |
| 7.04 | 0.00 | 7.04 | 0.54 | 6.50 |
| RDF based MSW Power Projects |
| 4.34 | 3.56 | 7.90 | 0.31 | 7.59 |

The above tariff will be applicable till the Tariff Order for MSW/RDF projects is issued separately once more data is available to fix the capital cost and tariff of such projects.

- Accordingly, on the directions of the Commission, this Staff paper has been prepared proposing to adopt the CERC RE Regulations, 2012 and the amendments thereof from time to time and the tariff determined by CERC from time to time for RE technologies and for MSW/RDF based projects pertaining to Manipur and Mizoram states. With the adoption of CERC RE Regulations, 2012 and its amendments thereof, the JERC M&M (Terms and Conditions for Tariff Determination from Renewable Energy Sources) Regulations, 2010 and its amendments thereof is repealed.

(H. THANTHIANGA)

Assistant Chief (Engg.)

Dated Aizawl

the 25th July, 2017